## Slide 1: sbRIO Control System
Summer 2012
Release 1.0
Christopher Gerth – Development Lead

## Slide 2: Overview
What?
  A customized, highly flexible, and extremely powerful control system for JSDC robots.
  Adaptable to any possible robot configuration
How?
  Through a generous donation of hardware and software by National Instruments
Why?
  To build groundwork for future members to have the engineering ability to execute any control system design

## Slide 3: Block Diagram
sbRIO
Robot mechanical interfaces
Host PC
Wifi Router
Other Ethernet-based Interfaces
Robot
Wireless Ethernet Link
USB link
Xbox controller
Xbox controller
Xbox receiver

## Slide 4: sbRIO
Basis of the System: National Instruments sbRIO 9642
  400 MHz Processor, 256MB long-term storage, 128MB program-accessible DRAM
  2M gate Xilinx Spartan FPGA
  110 3.3v DIO lines, 32 16-bit analog inputs, 4 16-bit pure voltage (not pwm) analog outputs
  32 High-current DIO’s (Run from external power supply at 6-30V)
  10/100BASE-T Ethernet, RS232 port
  Performs all major calculations and generates control signals for robot’s mechanical interfaces
  Many interfaces available, but only some are broken out through custom hardware plugs. These can be remade in future years as designs require more interfacing.

## Slide 5: sbRIO

## Slide 6: WIFI Router
Cisco Linksys E2500 Router/Wifi access point
  Supports B/G/N 2.4 GHz and 5.0Ghz Wifi
  Located on the Robot
  Facilitates rapid communication between Host PC and Robot
  Allows other IP-based peripherals (like cameras) to be interfaced.

## Slide 7: WIFI Router

## Slide 8: Host PC
Primary development tool
Should be club laptop
Runs NI’s Labview development environment
Interprets USB-based operator interfaces
Maintains server for all robot-PC communication
  Primary purpose is to have a library of shared variables which can be published over the main Ethernet Link
  Secondarily, serves as a monitoring point to view all data streamed into and out of the robot, as well as current controller status.

## Slide 9: Driver Interfaces
Xbox 360 controllers (2x)
Wireless, both communicate with PC through a special receiver (purchased with the controllers) and USB
Abstracted through a DirectX interface; Labview handles all communication interfacing.

## Slide 10: Driver Interfaces

## Slide 11: Software
Developed under NI’s graphical Labview environment.
Three main VI’s, controlling the three processors
  Host PC’s processor
  sbRIO’s processor
  sbRIO’s FPGA
Communication between these three asynchronous processes occurs via shared variables, or an FPGA FIFO.

## Slide 12: Software SubFunctions
VI running on the Host PC serves only to establish shared variable server, and transfer joystick data to the sbRIO
VI running on sbRIO maps joystick values to motor values with appropriate scaling
  Coordinates inputs from sensors with desired actions based on joystick/button input.
VI running on sbRIO’s FPGA handles all time intensive tasks, as well as routing all I/O data to the processor
  Currently, it tracks encoder positions and generates PWM signals
  Care needs to be taken when altering this design – recompiling the code takes over 10 minutes.

## Slide 13: Communication Block Diagram
Host PC
sbRIO Processor
sbRIO FPGA
Mechanical Interfaces
FIFO and Network Published Data
FIFO Registers
PWM, TTL 3.3v Logic, Analog IO
Upstream
Downstream

## Slide 14: Communication
Host PC <-> sbRIO Processor
  Both run co-dependent VI’s
  Utilize Shared Variables
    Stored primarily on Host PC
    Published to the Network
    FIFO data structure used for deterministic data transfer of critical data downstream from PC to sbRIO
    Host PC’s main loop runs slower than sbRIO’s so that FIFO does not clog up.
    Status information associated with the interface of the VI is transferred back to the PC periodically.

## Slide 15: Communication (IP)
Wireless Ethernet (WIFI) link is the primary control method
Static IP addresses
  sbRIO:192.168.1.73
  Router:192.168.1.72
  Subnet mask: 255.255.255.0
  Router Name (Not network name): Cisco73548
  SSID: iRobotics (hidden)
  Network key: *******************

## Slide 16: Communication (IP Security)
WAP2 Security
AES Encryption
  Other teams should not be able to sniff the packets
5 GHz radio disabled
SSID Not broadcasted
Wireless access restricted by MAC Address (only sbRIO and host PC allowed to connect)
  Other teams should have a very hard time connecting in to our network
No Firewall enabled (so don’t hook the internet up!)

## Slide 17: Communication
sbRIO’s Processor <-> FPGA
  Again, FIFO data structure used in downstream direction.
  FPGA runs much faster than processor
    Processor loop time = 10 ms
    FPGA loop time = 1.89 µs
  Upstream data flow is read by processor from buffered registers.

## Slide 18: FPGA
Fully Programmable Gate Array
Serves multiple functions
  Routes all I/O into processor
  Frees up processor from time-critical tasks
    Generates PWM signals
    Counts encoder ticks to keep track of wheel position

## Slide 19: Safety Cutouts
Maintaining safe operating conditions in the event of a communication failure is of paramount importance
  When VI is shut down, sbRIO passes high (invalid) signals to PWM outputs.
    Should be accounted for when designing systems which receive digital outputs
  When Ethernet is disconnected but VI continues to run, PWM signals go to 1.5% duty cycle (full stop)
    Possibility of reconnection, so sbRIO waits for new signals.
    Accomplished through a timeout monitor – if it takes more than 50ms to read in a shared variable, motors will shut down.
  Digital outputs remain unaffected
Independent “Emergency Stop” variable exists for a software-initiated stop.
Watchdog timer resets controller in even of processor glitch or communication shutdown
  Implemented for both CPU (in hardware) and FPGA (in HDL-software)

## Slide 20: Outputs (1)
PWM
  8 implemented in Hardware
  Three pin outputs: Ground, +5v, Signal
  Pulse lasts between 1 and 2 ms, and repeats every 20 ms.
    Results in a 500 Hz square wave, with duty cycle between 1% and 2%
    1.5% is full stop, 1% is full reverse, 2% is full forward.
    Victors might have to be calibrated, IFI systems seem to use a slightly different system.
Digital
  3.3v output, 3mA output per channel, 330mA total max.
Analog
  4 pure analog (not PWM) outputs.
  Range from -10v to 10v at 16 bit resolution, 3mA max drive.

## Slide 21: Outputs (2)
Relay (Spike)
  Same as Digital outputs, but grouped into two pins on the red and white wires in a PWM cable to drive a Spike Relay.
High-Current
  10 implemented in hardware.
  Sourcing output from an external power source at 6v to 30v
  250mA output per channel, possible to increase to 1.5 A with heatsinks
  Total Power not to excede 20A or supply’s maximum

## Slide 22: Inputs
Quadrature Encoder
  Each one consists of two inputs, one for each channel
  Counts normal two-bit grey code output, stores current position in FPGA register for use by the processor
  Utilizes XOR algorithm which accounts for small-angle rotations, and increments by four every full grey code cycle.
Digital
  3.3v input, 5v tolerant (compatible with TTL)
Analog
  Unimplemented in hardware, but 32 single ended or 16 differential inputs exist
  16 bit resolution on a -10v to 10v range
  Run at 250kSamples/sec (max frequency = 700kHz)

## Slide 23: Electrical Specs
sbRIO takes a 19-30v supply. We utilize the 24v boost power supply on the FRC power distribution board.
Take care to ensure digital ground remains isolated from battery/power supply ground.
Router takes 12 v. supply. Utilize the regulated supply on the FRC power distro board.
Fan for sbRIO also runs on 12v. It is electrically isolated from the main board.

## Slide 24: Software Design Philosophy
Three Main VI’s:
  Host Computer
  Processor
  FPGA
Main communication occurs between Host Computer and Processor
Utilizes NI’s Shared Variable system to manage multiple writers and readers from the same variables at the same time

## Slide 25: Example VI’s
Most of the VI’s are here, just to give a taste of what is involved
Most also are specific to this year’s (2012/2013) control system
  Holonomic drive (full continuous rotation of wheel assemblies)
  Currently unknown parameters for other outputs, two extra motor ports and four spike ports currently available.

## Slide 32: Shared Variables
Independent server runs on Host Computer
  It is a time and resource intensive process, so the sbRIO should not be responsible for it.
  Any VI running anywhere on the network can read or write to these variables
  For simplicity’s sake, try to only have one writer, otherwise it is difficult to debug

## Slide 33: Control Algorithm
A continual work in progress
Need to account for translational, rotational and arcing motions
Currently, case statement analyzes input and uses different algorithms for each type of motion.
Developing filters to smooth the transitions between each algorithm.
  Derivative-controlled to ensure timely response and smooth operation
Goal – a control scheme based in a single, continuous equation for maximum speed and accuracy.

## Slide 34: Software Simulation
“Debug Mode” part of sbRIO processor VI
Implemented for 2012/2013 year to simulate robot mechanical hardware
Keeps track of wheel positions and provides feedback info to control algorithm so there is a measurable error to correct for.
Allows for different correction rates, which simulates different physical robotics capabilities.

## Slide 35: Revision Updates
1.0 – Base Release